## Slide 1
Cytognosis Foundation · IGoR TA4
Element Teton vs. Cellanome R3200
Fixed-cell, high-plex molecular readout vs. live-cell functional profiling
 | ELEMENT TETON (AVITI24) | CELLANOME R3200
Cell state | Fixed (8% formaldehyde first) | Live throughout; viable and functional
Throughput / run | ~2M adherent or ~10M suspension cells | Tens of thousands of CellCage compartments
RNA + protein | 350 targeted RNA + up to 88 protein, in situ | Whole-transcriptome scRNA-seq, same cell
Readout | Avidite-base sequencing of barcodes (one snapshot) | Live imaging over days + off-chip NGS
Calcium imaging | None (cells are fixed) | Yes, multi-day (fast firing TBC)
Electrophysiology | None | None (calcium = optical proxy)
Longitudinal | No (single endpoint) | Yes (hours to weeks)
On-platform perturbation | No (reads out external screens) | Yes (chemical + pooled CRISPR)
Time-to-result | Under 24 h (~45 min prep) | Days to weeks + sequencing
Commercial status | Generally available; ~$424K | Launched 2026; also Psomagen service
Bottom line: complementary, not either/or. Cellanome for live function and on-platform perturbation; Teton for high-throughput, high-plex molecular readout. Neither performs true electrophysiology.
Notes: Sources: Element Biosciences Teton product sheet + user guide (elementbiosciences.com); Cellanome product/technology/neurobiology pages (cellanome.com); Psomagen R3200 overview; GenomeWeb AGBT 2026; Li et al., J. Immunother. Cancer (2025). Calcium-imaging temporal resolution on the R3200 (slow multi-day vs sub-second firing) is being confirmed with the vendor. Prepared 2026-06-19, IGoR TA4 context.